## Slide 1: Worst-case Stall Analysis for Multicore Architectures with Two Memory Controllers
Muhammad Ali Awan, Pedro F. Souto, Konstantinos Bletsas, Benny Akesson, and Eduardo Tovar

## Slide 2: Outline
Motivation
Overview
System Model
Analysis
Heuristics
Evaluation
Conclusions and future direction

## Slide 3: Motivation
App 1
App 2
App 3
App 4
Multi-core Platform
Interference
Resource Utilization
Timing Analysis
Computation
Energy
Weight
Scalability
Cost

## Slide 4: Overview
Memory controller
  Single memory controller (Memguard)
Things to improve on
  Platforms with two memory controllers (e.g., NXP QorIQ series)
Potential benefits
  Handles task dependencies
  Flexibility in memory bandwidth allocation

## Slide 5: Platform
Homogeneous multi-core platform
Multiple outstanding memory requests
Prefetchers and speculative units are disabled
Constant memory accesses time
Last-level cache is partitioned or private
Two shared memory controllers
Non-overlapping memory regions
Round robin arbitration
Performance monitoring counters per core for each controller

## Slide 6: Task Model
WCET
CPU Computation (Ce)
Memory accesses (Cm)
Controller one (Cm1)
Controller two (Cm2)
Constrained deadline
Sporadic tasks
No migration
Fixed priority Scheduling
CPU Computation and memory accesses do not overlap in time

## Slide 7: Memory Access Regulation Model
b
d
a
c
Core a memory access
Core b memory access
Core c memory access
Core d memory access
Memory accesses are regulated on both controllers (with aligned regulation periods)
Contention stall
b
d
a
c
Contention stall
b
d
a
c
Memory budget (Q) exhausted
a
a
a
a
Regulation stall
Budget exhausted
a
a
Regulation stall
Regulation period (P)
Each core has a per-controller budget
Regulation period
Controller one
Controller two
Uneven memory bandwidth (b = Q/P) across cores and controllers

## Slide 8: Main Idea
Core 1
Core 2
Core 3
Core 4
Controller 1
Controller 2
Core 1
Core 2
Core 3
Core 4
Controller 1
Controller 2
Partitioned Case
Shared Case

## Slide 9: Main Contributions
Show that existing techniques are not safe
Worst-case memory stall analysis for architectures with two memory controllers shared by all cores
Five stall-cognisant heuristics for i) memory-bandwidth-to-core assignment, and ii) task-to-core assignment

## Slide 10: Yao’s Analysis (1)
Contention stall
Regulation domination case: (b ≤ 1/m)
Maximize the regulation stall
Regulation stall
Regulation stall
Initial regulation stall
24
48
72
96
0
Memory accesses from core i
Memory accesses from other cores
CPU computation
Example
Q = 2
P = 24
m = 4
Cm = 5
Ce = 7

## Slide 11: Yao’s Analysis (2)
Example
Q = 12
P = 24
m = 4
Cm = 10
Initial regulation stall
24
48
72
96
0
a) Enough CPU computation
Memory accesses from core i
Memory accesses from other cores
CPU computation
Contention domination case: (b > 1/m)
Initial regulation stall
24
48
72
96
0
b) Not enough CPU computation

## Slide 12: Why Yao’s Analysis Fails with 2 Controllers
12
0
36
48
24
12
0
36
48
24
84
96
Contention stall
Access via controller 1
Stall = 24
Access via controller 2
Stall = 72
Cm1 = Cm2 = 12 Q1 = Q2 = 6 m = 4 P = 12

## Slide 13: New Stall Analysis
Case 2 (Contention dominant):
Case 1 (Regulation dominant):
Case 3 (both):

## Slide 14: Case 1 (Regulation dominant):
Regulation stall
Regulation stall
Contention stall
Regulation stall
Maximize the regulation stall for both controllers
Example
Q1 = 2
Q2 = 3
P = 24
m = 4
Cm1 = 5
Cm2 = 4
Ce = 7
24
48
72
96
0
Access via controller 1
Access via controller 2
CPU computation
Contention stall

## Slide 15: Case 2 (Contention dominant):
24
48
72
96
0
Phase 1
Phase 2
Phase 3
Access via controller 2
CPU computation
Contention stall
Access via controller 1
Example
Q1 = 18
Q2 = 18
P = 24
m = 4
Cm1 = 12
Cm2 = 5
Ce = 36
2a)

## Slide 16: Case 2 (Contention dominant):
Finish at the same time
Access via controller 1
Access via controller 2
CPU computation
Contention stall
24
48
72
96
0
Example
Q1 = 18
Q2 = 9
P = 24
m = 4
Cm1 = 6
Cm2 = 10
Ce = 0
24
48
72
96
0
Stall = 48
Stall = 42
2b)

## Slide 17: Case 3 (both):
Access via controller 1
Access via controller 2
CPU computation
Contention stall
Example
Q1 = 2
Q2 = 6
P = 12
m = 4
Cm1 = 4
Cm2 = 6
Ce = 0
Stall = 26
12
0
36
48
24
Stall = 30
12
0
36
48
24
Regulation stall
Regulation stall

## Slide 18: Schedulability Analysis
Schedulability analysis
Composite Task
Task under analysis
Jobs of higher or equal priority tasks that can preempt a task under analysis
Ce
Cm1 , Cm2
WCRT = Stall + Total demand (Ce + Cm1 +Cm2)
Standard response time analysis demand
Single task stall analysis
Stall Analysis
Ce
Cm1,Cm2
Upper bound on Stall
Q1, Q2

## Slide 19: Bandwidth Allocation and Task-to-core Assignment Heuristics
Five Heuristics
Even
- Each Core has an equal memory bandwidth share of both controllers
- First-fit bin packing for task-to-core assignment
Uneven
- Initially each core gets an equal memory bandwidth share for each controller - Trim-off memory bandwidth from both controllers, if tasks are not schedulable with equal memory bandwidth
- Use this trimmed bandwidth to schedule remaining tasks
Greedy-fit
- Assign all memory bandwidth from both controllers to first core
- Iterate over all tasks to assign as many as possible
- Trim the memory bandwidth for each controller on this core to assign to the next core and assign remaining tasks to this core
Humble-fit
- Similar to greedy fit, except move to next core upon first failure
Memory-fit
- Assign a task to the core that requires the least additional memory bandwidth
Priority assignment: Audsley’s algorithm (not necessarily optimal)

## Slide 20: Evaluation
Synthetic workload generated with the UUnifast-discard algorithm
Inter-arrival times with log-uniform distribution (10-100 ms)
Implicit deadlines
Memory accesses for each controller are generated randomly
1000 task-sets for each set of input parameters
Task-set is sorted in descending order of utilization
Compare weighted schedulability

## Slide 21: Results
Partitioned memory controllers among cores
  Half of the cores assigned to each controller
  Each heuristic adapted for this arrangement
  “Yao-” prefix followed by the heuristic’s name
Shared memory controllers
  “MC-” prefix followed by each heuristic

## Slide 22: Results

## Slide 23: Conclusions and Future Directions
Existing stall analysis for single-memory controller systems is not applicable to dual-controller systems
We developed safe analysis for the latter case
Partitioning of the controllers performs better than sharing in our experiments:
  but it may not always be practical
    resource sharing across controller domains
    Tasks with very unbalanced bandwidth requirements.
  We quantify the performance tradeoff
In the future, we are considering extending this to a mixed-criticality context (Vestal model)

## Slide 24: Questions ?