## Slide 1: Recovery-Time Considerations in Real-Time Systems Employing Software Fault Tolerance
Anand Bhat*, Soheil Samii†, Raj Rajkumar*
*Carnegie Mellon University
†General Motors R&D

## Slide 2
Motivation
System Model
  Task Model
  Platform Model
  Fault Model
Recovery Time Analysis
Redundant-Task Type Assignment
Task partitioning with Recovery Time Constraints
  RTT Heuristic
  Simulated Annealing Approach
  Evaluation
Conclusions and Future Directions
Outline

## Slide 3: Motivation
Real-time systems like cars are inherently safety-critical.
To ensure safety, computing systems must be fault-tolerant.
Typically fault tolerance is achieved with the help of redundancy.

## Slide 4: Traditional Redundancy Approaches
Hardware replication is inefficient in terms of
  Cost
  Weight
  Space
Hence, there is a need for adaptive cost-optimized software fault tolerance solutions.
Hardware(HW) Replication
  Triple Modular Redundancy (TMR)
HW1
HW2
HW3
VOTER
Input
Output

## Slide 5: Software Fault Tolerance
Software replication can be of different types.
  Active Replication: All tasks perform all operations
  Primary Backup Approach: Only primary performs all operations
There is built-in trade-off between time required to recover from failure (Recovery Time) to system resources utilized.

## Slide 6: Recovery Time Requirements
The recovery time for a task depends on:
  redundant-task type assignment,
  task allocation, and
  scheduling policy.
Each task can have a different recovery time requirement (RTR), i.e. the number of deadlines that can be missed in the case of a failure.
The redundant-task type assignment and allocation must be selected to meet the RTR for each task.

## Slide 7
Motivation
System Model
  Task Model
  Platform Model
  Fault Model
Recovery Time Analysis
Redundant-Task Type Assignment
Task partitioning with Recovery Time Constraints
  RTT Heuristic
  Simulated Annealing Approach
  Evaluation
Conclusions and Future Directions
Outline

## Slide 8
Periodic Task Model (Ci, Ti, Di)
  Ci: Worst-case execution time
  Ti: Period
  Di: Deadline (Di = Ti)
  Ui: Utilization (Ui = Ci/Ti)
Fixed Priority Preemptive Scheduling
  Rate Monotonic Scheduling (RMS)
Worst-case completion time (WCCTi): The worst-case time from arrival to completion of task.
A task is said to be schedulable if its WCCTi ≤ Di.
Computation Model (1 of 2)

## Slide 9
Throttle
Control (TC)
(Ui = 0.3)
(2 copies)
RTR = 1
Steering
Control (SC)
(Ui = 0.6)
(1 copies)
RTR = 3
Brake
Control (BC)
(Ui = 0.4)
(2 copies)
RTR = 0
Video
Playback (VP)
(Ui = 0.8)
(0 copies)
HVAC
(Ui = 0.4)
(0 copies)
Audio Playback
(AP)
(Ui = 0.8)
(0 copies)
Computation Model (2 of 2)
Sample Task Set
Critical tasks
Non-critical tasks

## Slide 10
Fault Model (1 of 2)
Crash Faults (fail-stop)
  Hardware,
  Operating system and
  Process crashes
Communication Assumption:
  The network is analyzable and every message in the network is delivered within a known delay bound  or not delivered.
Fault detection Assumption:
  Replicas monitor the status and health of the primary, for example, by using heartbeats

## Slide 11
We assume three types of Redundant-Task Type Assignment
Fault Model (2 of 2)
Type of Task | Scheduled | Read and Process Inputs | Calculate State | Perform Calculations | Produce Output
Primary |  |  |  |  | 
Active Replica |  |  |  |  | 
Hot Standby |  |  |  |  | 
Cold Standby |  |  |  |  | 
Primary (0.1)
Hot (0.1)
Cold (0.1 OR 0.05)

## Slide 12
Given N nodes, and a task set = {1, 2, ..., n}, where every task has an application-dependent recovery-time requirement RTRi
  derive bounds on the recovery time for each redundant-task type,
  decide a redundant-task type, i.e., active, hot or cold, and
  find an allocation where all tasks satisfy their recovery-time requirements while minimizing the number of nodes used for allocation.
Goals

## Slide 13
Motivation
System Model
  Task Model
  Platform Model
  Fault Model
Recovery Time Analysis
Redundant-Task Type Assignment
Task partitioning with Recovery Time Constraints
  RTT Heuristic
  Simulated Annealing Approach
  Evaluation
Conclusions and Future Directions
Outline

## Slide 14: Recovery Time Bounds – Active Replicas
Active replicas run alongside the primary
They allow seamless fault recovery
Primary
Active
Replica
Time
Primary
Failure
Implicit
Recovery

## Slide 15: Backup Following the Primary
Uncontrolled Release offsets
Backup
Following
the Primary

## Slide 16: Recovery Time Bounds - Hot Standbys

## Slide 17: Recovery Time Bounds - Cold Standbys

## Slide 18
Motivation
System Model
  Task Model
  Platform Model
  Fault Model
Recovery Time Analysis
Redundant-Task Type Assignment
Task partitioning with Recovery Time Constraints
  RTT Heuristic
  Simulated Annealing Approach
  Evaluation
Conclusions and Future Directions
Outline

## Slide 19
A recovery time of a redundant task must satisfy the RTR of the task.
For RTR = n,
  RT ≤ (n+1) T
We prioritize Cold and Hot standbys over Active replicas since they are more resource efficient.
Redundant-Task Type Assignment

## Slide 20
Redundant-Task Type Assignment
The task allocation directly affects the choice of redundant-task type assignment.

## Slide 21
Motivation
System Model
  Task Model
  Platform Model
  Fault Model
Recovery Time Analysis
Redundant-Task Type Assignment
Task partitioning with Recovery Time Constraints
  RTT Heuristic
  Simulated Annealing Approach
  Evaluation
Conclusions and Future Directions
Outline

## Slide 22
Problem definition:
Given a task set, assign every task to a node such that
  No primary or any of its standby is allocated to the same node while minimizing the number nodes used for allocation.
Fault-Tolerant Task Allocation
Node
1
Goal: Avoid common-mode failures while optimizing cost, weight and space.
Primary (0.1)
Hot(0.1)
Node
1
Primary (0.1)
Node
2
Hot (0.1)
Primary (0.1)
Placement Conflict
No Placement Conflict

## Slide 23
Finding an optimal task allocation given an arbitrary task set is NP-hard.
Hence we use heuristics for task allocation.
Any Task Allocation Heuristic has 2 steps
  Task Ordering
  Node Ordering
Task Allocation Heuristics

## Slide 24
Task Ordering – Tiered by increasing RTR constraints and descending order of Task Utilization (Ui) in each tier for critical tasks.
RTR-tiered (RTT) heuristic (1 of 3)

## Slide 25
RTR-tiered (RTT) heuristic (2 of 3)
Node Ordering – Non increasing total task utilization order excluding nodes with placement conflicts

## Slide 26
RTR-tiered (RTT) heuristic (3 of 3)
Non –critical tasks are ordered in decreasing utilization values and assigned last after accounting for lower replica utilizations

## Slide 27
Evaluation: Standby Distribution

## Slide 28
Evaluation : Node Usage

## Slide 29
Applying Simulated Annealing
Problem formulation:
Given n tasks (1, 2, ..., n), with utilization (u1, u2, ..., un), where ui ≤ 1, find the number of nodes M of size 1 that are needed to pack all tasks such that a primary task and its corresponding redundant copies obey the placement constraint of not being co-located on the same node and optimizing the following cost function

## Slide 30
Simulated Annealing

## Slide 31
Generating Random Solutions (1 of 2)
We randomly move a single task from a randomly-selected node k to another randomly-selected node l.

## Slide 32
Generating Random Solutions (2 of 2)
We randomly select two tasks currently located in two different bins and swap them.

## Slide 33
Evaluation: Node Usage

## Slide 34
Evaluation: Execution Time

## Slide 35
Conclusions and Future Work
RTR of a task can be mapped to a redundant-task type assignment.
Recovery-Time Tiered (RTT) prioritizes the RTR constraints in the task allocation sequence and produces better allocations than the TPCDC+R
The simulated annealing method was adapted to solve the fault-tolerant task allocation optimization problem it produces allocations utilizing fewer computing resources than the proposed heuristics, at the cost of substantial run-time.

## Slide 36: Thank you

## Slide 37: Questions?