## Slide 1: Verifying Weakly-Hard Real-Time Properties of Traffic Streams in Switched Networks
Leonie Ahrendts, Sophie Quinton, Thomas Boroske, Rolf Ernst
TU Braunschweig
ECRTS in Barcelona, July 5th 2018

## Slide 2: Introduction
Modern embedded systems are often distributed.
Processing elements (PE) are connected through data buses or switched networks.
PEs send traffic streams to remote PEs.
PE
PE
PE
Traffic streams are subject to real-time (RT) requirements:
hard = no deadline misses
formal RT guarantees
high cost
weakly-hard = at most m deadline misses in k transmissions
formal RT guarantees
intermediate cost
but functional robustness required
e.g. image processing
control algorithms

## Slide 3: Related Work
Can we compute WHRT guarantees for RT networks?
No.
PE
PE
PE
What can we compute?
maximum end-to-end latency
CPA
  event stream propagation
Network Calculus
  propagation of workload & remaining service
local WHRT guarantees
TWCA
  general system model
  compatible with CPA
Individual works
  restricted system model
  high accuracy
Idea: Combine CPA + TWCA to compute end-to-end WHRT guarantees.

## Slide 4: How to combine CPA & TWCA?
Traffic stream = distributed event-triggered task chain on SPNP-scheduled components
computation of output event streams
CPA
computes output event streams
compatible with different component-related timing analysis techniques
component-related analysis
TWCA
computes WHRT guarantees for tasks
Major open issue:
TWCA expects an event stream to be decomposed into streams of typical and overload events! CPA is agnostic of these event types!

## Slide 5: CPA – Interface
input event stream
bounded by
output event stream
bounded by
CPA computes based on local analysis results:

## Slide 6: TWCA – Interface
lower and upper bounds for:
events | , | 
overload events | , | 
typical events | , | 
events |  | 
overload events |  | 
typical events |  | 
TWCA principle:
Only typical events  Task set is schedulable.
Typical events + overload events  Transient overload phases.
Deadline misses scale with the number of overload events.
Provided WHRT guarantee:
Task does not miss more than m deadlines in k consecutive jobs.
?
?
?
missing event stream propagation !

## Slide 7: TWCA – Interface
now generalized TWCA to cover:
+
state-of-the-art TWCA requires:
= +
Relation between and
e.g. minimum distance between any two events!

## Slide 8: TypicalCPA – Output event stream computation
output event model | computation method | 
 | CPA | 
 | CPA under the assumption that only typical events enter the system | 
 | Definition of a difference operation such that the resulting overload event arrival curve is safe upper bound on overload event arrival | Theorem 23 Theorem 24 including an efficient computation method
output event model | computation method | 
 | CPA | 
 | CPA under the assumption that only typical events enter the system | 
 |  | Theorem 23 Theorem 24 including an efficient computation method
?
?
?
Notes: backup Folie hinzufügen

## Slide 9: TypicalCPA – Difference operation

## Slide 10: Overview
TypicalCPA
CPA
Difference operation
Derive inital input event models
Perform local SPNP analysis
Convergence of event models?
Output: event models
Update output event models
CPA
Derive inital typical input event models
Perform local SPNP analysis
Convergence of event models?
Output: typical event models
Udpate output event models
Difference operation
Difference operation
Difference operation
Difference operation
TWCA
yes
yes
no
no

## Slide 11: Evaluation
Automotive backbone network
case study with (anonymized) data from Daimler [Thiele et al. 2014]
    Switched Ethernet
    different topologies
    periodic traffic streams:
    50 control streams + 4 camera streams
addition of sporadic control traffic
    camera streams are robust towards a limited number of deadline misses
    configurable number of sporadic control streams
sporadically bursty event arrival
here:
random generation of incomplete data:
path generation
payload sizes, periods
Notes: b=3 special case (discard possibly)

## Slide 12: Evaluation
100 Mbit/s
1 Gbit/s
Quadruple Star
Double Star
Tree

## Slide 13: Evaluation
WHRT guarantees for camera streams
→ 50 generated systems with quadruple star topology
100 Mbit/s
1 Gbit/s
+ 5 sporadically bursty control streams
+ 10 sporadically bursty control streams
m
m
average
median =
m
Notes: what is the actual problem / corner cases / priorities , SPNP
improvement compared to worst case (how many of the lossy cases can be handled?)

## Slide 14: Evaluation
Details on non-zero WHRT results for camera streams with k = 100 (set of 50 systems)
 | m |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 19 | 20 | 21 | … | 100
5 overload streams |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 6x | 5x | 15x |  | 2x |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 6x | 3x | 22x | 1x | 1x | 6x |  | 1x |  |  |  | 1x |  | 1x |  |  |  |  |  | 
10 overload streams |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 2x | 2x | 31x | 1x | 6x |  |  |  |  | 2x | 1x |  | 1x |  | 1x | 1x |  |  |  | 3x
 |  |  |  | 15x | 5x |  | 2x | 1x | 1x | 2x |  | 5x |  | 2x | 4x | 2x |  |  |  |  | 23x
 | m |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 19 | 20 | 21 | … | 100
5 overload streams |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 6x | 5x | 15x |  | 2x |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 6x | 3x | 22x | 1x | 1x | 6x |  | 1x |  |  |  | 1x |  | 1x |  |  |  |  |  | 
10 overload streams |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 2x | 2x | 31x | 1x | 6x |  |  |  |  | 2x | 1x |  | 1x |  | 1x | 1x |  |  |  | 3x
 |  |  |  | 15x | 5x |  | 2x | 1x | 1x | 2x |  | 5x |  | 2x | 4x | 2x |  |  |  |  | 23x
With hard RT systems, designs must be rejected even if only very few deadline misses occur in k=100 jobs of camera streams.
With weakly-hard RT systems, these designs are valid depending on (m,k)-requirements!
how often m=2 was observed for a camera stream
Notes: occasionally „bad“ results; most cases have a small miss rate

## Slide 15: Conclusion
First compositional analysis framework, which provides (m,k)-guarantees for multi-component real-time systems
        CPA (Compositional Performance Analysis) + TWCA (Typical Worst Case Analysis)
        Extended event propagation
        Generalized TWCA (done for SPNP)
Application to real-time networks
        automotive case study
Future work
        extension to cover also SPP scheduling
        increased accuracy

## Slide 16: Evaluation
[Thiele et al. 2014]