## Slide 1: Routing Algorithms for IEEE802.1Qbv Networks 15th International Workshop on Real-Time Networks
Naresh Nayak
Frank Dürr, Kurt Rothermel
27.06.2016

## Slide 2: Communication in Networked Control Systems (NCS)
Network
Networked Control Systems
Sensors, Actuators & NCS-Controller
Communication network
NCS Controller
Sensor
Actuator
Application Domains
Industrial automation
Automotive etc.
Real-time communication requirements
Upper bounds on latencies and jitter
Motion controlled systems
  Latency < 65µs, Jitter < 1µs
Real-time
Network

## Slide 3: Transition to IEEE 802.3 (Ethernet) Networks
Emergence of many field-bus systems
Incompatibilities between field-buses
Loss of real-time guarantees when interoperated
Dedicated solution, expensive
Transition to IEEE 802.3 (Ethernet) n/w
High performance, low cost
Ubiquitous
 But designed only for best effort service
Initiatives for real-time capabilities for Ethernet
IEEE – Time-sensitive Networking Task Group
  IEEE 802.1AS – Clock Synchronization
  IEEE 802.1Qat – Stream Reservation Protocol
  IEEE 802.1Qbu – Frame Pre-emption
  IEEE 802.1Qbv – Enhancements for scheduled traffic
  among others
IETF – DetNets Working Group
  Real-time properties over WAN

## Slide 4: IEEE 802.1Qbv – Enhancements for scheduled traffic
Traffic class 0
Traffic class 5
Traffic class 6
Traffic class 7
Queues for best-effort (BE) traffic
Queue for scheduled traffic (ST)
Gate Driver
Gate
Gate
Gate
Gate
Output selector
Switch port
Scheduled Traffic
Gate
Gate
Gate
Gate
Best-effort Traffic
How to handle scheduled traffic using this mechanism?
t1 close BE Gates
t2 open ST Gate
... …
tn …
repeat
Reserved queue(s) for scheduled traffic and best-effort traffic
Time-based gating program

## Slide 5: Routing & Scheduling Problem in IEEE 802.1Qbv networks
Isolate time-triggered flows to bound queuing delays
  Spatial domain (Routing)
  Temporal domain (Scheduling)
Flows routed using off-the-shelf routing algorithms
Subsequently scheduling over every link traversed by the flow
Hosts
Switches
Src for F1
Dst for F1
Dst for F1
Src for F2
Dst for F2
Link Transmission Schedule

## Slide 6: State-Of-The-Art Scheduling Approaches
Approaches based on Satisfiability Modulo Theories
  Steiner RTSS-2010, Craciunas et al. RTNS-2016
  Model TSN scheduling problem using satisfiability constraints
  Computes one feasible schedule
Mapping TSN Scheduling Problem to other known scheduling problems
  No-wait Job-shop Scheduling Problem – Dürr et al. [RTNS-2016]
  Resource Constrained Scheduling Problem – Hanzalek et al. [IEEE TII. 2010]
  Optimizes schedule length (Makespan)
Relation between routing algorithms & scheduling algorithms not yet studied with respect to IEEE 802.1Qbv

## Slide 7: Contributions in this paper
Explore the impact of routing time-triggered flows on their schedulability
  Scope restricted to scheduling using the No-wait Job-shop Scheduling Problem
Identify metric(s) for routing algorithms that consider also the schedulability and propose tailored routing algorithms for IEEE802.1Qbv network
  Algorithm 1: Maximum Scheduled Traffic Load (MSTL) Based Routing
  Algorithm 2: Maximum Scheduled Traffic Load (MSTL) + Hops Based Routing
Evaluations show 30-60% improvement in schedulability of time-triggered flows using proposed algorithms compared to benchmark algorithms

## Slide 8: System Model
IEEE 802.1AS for precise clock synchronization
Real-time traffic scheduling through time-triggered gates (IEEE 802.1Qbv)
Network Controller Solves scheduling/routing problem
Global view onto network & real-time flows
Add/remove time-triggered real-time flows
(src, dst, cycle time, packet size)
Schedule and route config.
Explicit forwarding path control
(IEEE 802.1Qca or OpenFlow)

## Slide 9: No-wait Job-shop Scheduling Problem in Operations Research
Well-known problem in operations research – NP-hard
Scheduling set of jobs (sequence of operations) on a set of machines in shopfloor
  Compute schedules of minimal length (makespan)
Example: 2 machines (M1, M2) executing 3 jobs (J1, J2, J3)
  Job J1: M1 (2 time units) Job J2: M2 (2 time units), M1 (1 time unit) Job J3: M1 (3 time units), M2 (1 time unit)
M1
M2
M1
M2
J1
J2
J3
makespan = 6
M1
No-wait constraints
J1
J2
J3
makespan = 7
M2
M1
M1
M1
M2

## Slide 10: NW-JSSP in IEEE 802.1Qbv Networks
Host network interfaces & switch ports → Machines (performing forwarding operations)
Time-triggered flows → Jobs
  Seq. of forwarding operations by switch ports & network interfaces = Routes of the flows
  Time for each operation = Serialization time for the pkts of the flow on the corresponding link
Src A
Src B
Dst A
Dst B
Src C
Dst C
l1
l2
l3
l4
l5
l6
l7
l1
l4
l5
l2
l4
l6
l3
l4
l7
Flow C
Flow B
Flow A
Flowspan
TCycle
Slack
Refer Dürr et al. RTNS-2016 for more details

## Slide 11: Problem Statement – Routing of Time-triggered Flows
Number of hops used as the metric
  Shortest path routing, Equal-cost Multi Pathing etc.
  Agnostic to the underlying scheduling problem of time-triggered flows
  Leads to bottleneck links → Infeasible schedules i.e. Flowspan > TCycle
Goal: Reduce bottlenecks & improve schedulability
  Minimize flowspan & improve schedule slack
  Maximum Scheduled Traffic Load (MSTL) as metric
    Maximum amount of scheduled traffic sent out over any of the port per scheduling cycle
100
75
50
75+50=125
MSTL = 125 bytes

## Slide 12: Problem Statement – Routing of Time-triggered Flows
Number of hops used as the metric
  Shortest path routing, Equal-cost Multi Pathing etc.
  Agnostic to the underlying scheduling problem of time-triggered flows
  Leads to bottleneck links → Infeasible schedules i.e. Flowspan > TCycle
Goal: Reduce bottlenecks & improve schedulability
  Minimize flowspan & improve schedule slack
  Maximum Scheduled Traffic Load (MSTL) as metric
    Maximum amount of scheduled traffic sent out over any of the port per scheduling cycle
100
75
50
MSTL = 175 bytes
100+75

## Slide 13: Relation between Flowspan & MSTL
Evaluation Scenario
Erdős-Rényi Topology
  10 Switches
  50 Hosts
Time-triggered flows
  Hosts and destination is selected with uniform distribution
  Size of flow uniformly distributed between 300-1500 Bytes
Flowspan increases with an increase in the MSTL

## Slide 14: Algorithm 1: MSTL-Based Routing – Terminologies & Objective
ILP Inputs
Network Topology,
Time-triggered flows,
ILP Variables
Routes,
Max. Scheduled Traffic Load, MSTL
Auxiliary Variables,
  To handle Multicasts
ILP Objective
Minimize: MSTL

## Slide 15: MSTL-Based Routing – Constraints
Routing Constraints (For all flows i)
Load Constraints (For all links j)
Auxiliary Constraints (For all flows i & links j)

## Slide 16: Algorithm 2: MSTL-Based + Hops based Routing
MSTL-based routing considers only the scheduled traffic
May route flows over longer paths
  Acceptable, if it indeed reduces the MSTL
  Undesirable, if it has no impact on MSTL
Extend MSTL-based routing to also incorporate length of allocated route
  Modified objective
Minimize

## Slide 17: Evaluation Setup
Commodity hardware for network controller
  Intel Xeon E5-1650 (2 x 6 processor cores)
  16GB RAM
Evaluation over randomized graph models & randomized traffic patterns
  Erdős-Rényi Model & Barabási-Albert Model
    50-100 hosts and 10-20 switches
  Varying number of flows (200-1000)
    Source and destinations chosen using uniform distribution

## Slide 18: Evaluations
Evaluation Scenario
Erdős-Rényi Topology
  10 switches & 50 hosts
Routing using benchmark algorithms and proposed algorithms
Subsequent schedule computation using No-wait Job-shop Scheduling
Flowspan reduction of MSTL+Hops: Max. 60% (Avg. 38%) against SP Max. 30% (Avg. 20%) against ECMP

## Slide 19: Evaluations
Evaluation Scenario
Erdős-Rényi Topology
  10 switches & 50 hosts
Varying number of flows (200-1000)
Runtime evaluations: MSTL-based algorithm scales linearly compared to the exponential increase in the MSTL+Hops based algorithm

## Slide 20: Related Work
IEEE 802.1Q & IEEE 802.1qa
  Rapid-spanning tree protocol
  Multiple-spanning tree protocol
  Shortest-path bridging
Laursen et al. – Routing Optimization of AVB Streams in TSN Networks [RTN-2016]
  Routing optimization of AVB Streams to meet the timing constraints
Nayak et al. – TSSDN [RTNS-2016]
  Combined solution of routing & scheduling problem
  Coarse grained schedules instead of link-based schedules

## Slide 21: Conclusion & Future Work
Conclusion
Explored the relation between routes of time-triggered flows and their schedulability
Motivated the need for metrics (in addition to number of hops) to incorporate awareness to scheduled traffic in the routing algorithms
Presented two ILP-based routing algorithms yielding up to 30-60% improvement in the schedulability compared to standard routing algorithms
Future Work
Develop heuristics for improving runtimes of the routing algorithms
Extend the algorithms to handle routing of dynamic flows
Generalize the algorithms to be applicable for other scheduling approaches as well